## Slide 1: Brain Norm

## Slide 2: Week 1

## Slide 11: Week 2 & 3
Convert Homer3 preprocessed .snirf file to MNE compatible .snirf.
Run a GLM from Homer3
Check what is going wrong with the modified pruning files.
Try to validate .snirf files without processing it through Homer3

## Slide 12: Convert Homer3 preprocessed .snirf file to MNE compatible .snirf
SNIRF files exported from Homer3 are partially compatible with MNE, but not fully compliant with the strict SNIRF standard that MNE expects.
You can load them in MNE after cleaning or patching the file but not directly — because of metadata and label mismatches.

## Slide 13
Issue | Homer3 Export Behavior | What MNE Expects
TimeUnit | Often missing or None | Must be "s" (seconds)
Channel Type Labels | Can be "hrf hbo", "hbt", "hrf hbr" etc. | Must be exactly "hbo", "hbr", "fnirs_od", etc.
Probe Labels | May include None, empty strings, or duplicated names | Must be valid UTF-8 strings, all unique
Stimulus Events | Sometimes unnamed or duplicated | Must have a non-empty "name" field

## Slide 14
The demo dataset is downloaded directly from the official MNE-Python dataset server passes the validation.

## Slide 15
Your Homer3-exported .snirf file exists and loads, but it fails SNIRF validation according to pysnirf2.validateSnirf().

## Slide 16: Generate a MNE compatible .snirf

## Slide 19: Week 4
Export the .snirf file without block_avg
Run Homer3 without gui to avoid export bug
Remove HbT channel (not recognized by MNE)
Fix metadata
Validate snirf file

## Slide 20: Validate file and check file loading in MNE

## Slide 21: Export the .snirf file without block_avg

## Slide 22: Run Homer3 without gui to avoid export bug

## Slide 23
Loading SNIRF: sub-bndy_ses-tp1_task-arith_run-1_nirs_with_events.snirf
Running hmrR_PruneChannels...
hmrR_PruneChannels: excluded channels [ 1 2 3 4 7 10 11 12 16 17 26 27 28 33 37 45 1 2 3 4 7 12 16 17 26 27 28 33 ] based on dRange=[ 0.005 0.9 ] at wavelength 2
Running hmrR_Intensity2OD...
Running hmrR_MotionArtifactByChannel...
Running hmrR_MotionCorrectSpline...
Running hmrR_MotionCorrectWavelet...
Loading /Users/divijnalge/Library/CloudStorage/OneDrive-NanyangTechnologicalUniversity/ntu/Brain Norm/Homer3/Install/db2.mat
*****************************************
** DWT Extension Mode: Periodization **
*****************************************
Running hmrR_BandpassFilt (hpf = 0.010, lpf = 0.200)...
Running hmrR_OD2Conc...
Saving continuous HbO/HbR SNIRF:
output_preproc_hb.snirf
Done.

## Slide 24: Remove HbT channel (not recognized by MNE)

## Slide 25
(nirs) divijnalge@Divijs-MacBook-Pro MNE % python homer3_to_mne_compatible.py
Input SNIRF: /Users/divijnalge/Library/CloudStorage/OneDrive-NanyangTechnologicalUniversity/ntu/Brain Norm/Brain_Norm_Files/fNIRS preproc/BN_DY/ses-tp1arith/nirs-homer3/3cond/output_preproc_hb.snirf
Will write: /Users/divijnalge/Library/CloudStorage/OneDrive-NanyangTechnologicalUniversity/ntu/Brain Norm/Brain_Norm_Files/fNIRS preproc/BN_DY/ses-tp1arith/nirs-homer3/3cond/output_preproc_hb_mne.snirf
Unique dataTypeLabel values BEFORE: ['HbO', 'HbR', 'HbT']
Total channels: 138
Keeping 92 channels (HbO/HbR only)
Dropping 46 channels (e.g. HbT)
Done.

## Slide 26: Fix metadata – Error 1
TypeError: iteration over a 0-d array
...
for idx, dign in enumerate(digname):

## Slide 27: Fix metadata - warnings

## Slide 29: Fix metadata – Error 2
ValueError: np.float64(nan) is not in list
...
wavelength_idx = wavelengths.index(raw_wavelengths[idx - 1]) + 1

## Slide 31
Run glm from MNE
Run glm from Homer3 without gui
Use the customized pruning scripts to do above

## Slide 32: Running GLM in MNE

## Slide 33: Subject – BNKG; Run 1